## Slide 1: ENGI 301 GuitarHero Proposal
February 19, 2024
Brian Mercado

## Slide 2: Background Information
An embedded system that reads guitar music PDF’s and displays the TAB of each chord of the song on an 16x32 LED panel
  Sheet Music PDF Reader: https://github.com/aashrafh/Mozart
  Additions:
  Will read name of guitar chords and BPM
  Will code array of LED’s that will represent the guitar tab for each chord
  Will display detected chord name with its LED representation
  I recently joined the Mariachi Luna Llena and am a guitarist. However, I have not played guitar in an ensemble setting and need to learn new chords. This will greatly help me learn necessary chords

## Slide 3: System Block Diagram
OSD335x-SM SiP contains: AM3358 TPS65217C TL5209 EEPROM
µUSB Host Connector
5 volts
USB0
MMC0
µSD Card Connector
IS-P6-8S-SMD3528
16x32 LED Matrix Panel
GND
Potentiometers
LED
Cape Headers

## Slide 4: Power Block Diagram
OSD335x-SM SiP contains: AM3358 TPS65217C TL5209 EEPROM
µUSB Host Connector
5 volts
USB0
16x32 LED Matrix Panel
Up to 2.5A max
5V
5 volts
5V 4A (4000mA) switching power supply
Female DC Power adapter - 2.1mm jack to screw terminal block
3.3V
LED

## Slide 5: Components / Budget
Component | ENGI301 to Buy? | Cost
16x32 LED Matrix Panel https://www.adafruit.com/product/420 | Yes | 24.95
5V 4A (4000mA) switching power supply https://www.adafruit.com/product/1466 | Yes | 14.95
Female DC Power adapter - 2.1mm jack to screw terminal block https://www.adafruit.com/product/368 | Yes | 2.00
Potentiometers | No | 
LED’s | No | 
Potentiometer | No | 
Button | No | 
See Next Slide for Instructions

## Slide 6: Software Block Diagram
Update Song List
Browse through songs
Select song
Select tempo
Play through song
Button Press
< 3s
> 3s
Display song title
Cycle through songs with potentiometer
> 3s
Button press
Display BPM
Use potentiometer to change BPM
Run on startup and check repository of music for new music
Run new music through pdf -> music program
Add to list of music ready to play
Display guitar string represented as lines
Press button to start
Blinks tempo using LED
Displays chords according to music sheet and tempo
Button press
Displays “End”
> 3s
< 3s
Pause/Resume
Power up